## Slide 1: Basic Health Monitoring Station
Project Guide : Madam Karma Kelzang Eudon
External Guide : Mr Kinley Penjor
Date: 19/09/2025
Group 3 Members:
1.Arun Sanyasi
2.Tashi Chozom
3.Sherab Zangmo

## Slide 2: Table of Contents
Introduction
Background
Problem Statement
Aim
Objectives
Literature Review
Methodology
Proposed system overview
System Flow Chart
Expected outcomes
Bill of Materials
Budget Calculation
Power Calculation
Work Plan

## Slide 3: Introduction
Health monitoring is vital for early detection and prevention of diseases (World Health Organization, 2020). A Health Monitoring Station simplifies this by measuring key parameters and to display, it provides quick and reliable results, making healthcare more accessible and convenient (Kumar et al., 2022).

## Slide 4: Background
Lifestyle diseases are increasing, while healthcare access is often limited (WHO, 2022). Measuring vitals like heart rate, SpO₂, temperature, and BMI traditionally required multiple devices. Advances in biomedical sensors and microcontrollers now enable these in one compact system (Sharma & Singh, 2021), supporting preventive care and monitoring (Chen et al., 2019).

## Slide 5: Problem Statement
In our college, the Health Assistant currently uses separate devices to check vital signs. A single Health Monitoring Station that measures pulse rate, respiratory rate, SpO₂, temperature, and BMI in one system can speed up health check-ups. Before going to the Health Assistant, students and staff can use the station for pre-checks, which will help medical personnel quickly proceed with the necessary examinations.

## Slide 6: Aim and Objectives
Aim:To design a health monitoring system that measures four vital signs and BMI for basic check up.
Objectives:
To design an integrated system for the measurement of pulse rate, respiratory rate, SpO₂, temperature, and BMI.
To publish vital signs and health insights using ESP32 and Raspberry Pi.
To install the system in the infirmary for quick and easy health check-ups.

## Slide 7: Literature Review
Sl.No | Title | Authors/Institution | Features | Key findings | Limitations
. | Real-Time Vital Signs Monitoring System | Srishti Dhingra, Madhuri Sharma, Hitesh Arora, Anupam Misra, Surabhi Nayak Department of CSE, SRM-IST, NCR Campus, Modinagar | Measures heart rate, ECG, breathing, skin response, temperature LCD + web app for display and monitoring IoT-enabled data transfer | Provides Real-time and continuous monitoring Remote access by doctors through web app Low cost and portable | Limited parameters (no SpO₂, BP). Motion artifacts, calibration. No strong data security. Prototype stage
2. | Automated Body Mass Index Assessment Device | Horsfall, Otelemate M. Yaabari, Monday University of Port Harcourt | Used MHT1 load cell and HC-SR04 ultrasonic sensor Includes LCD display and alarm system for Obesity indication 12V adapter as backup power. | Provides accurate BMI measurements Automate the calculation User friendly | Tested on a small sample(10 people,age of 18-36) Device scope limited to BMI

## Slide 8: Literature Review
Sl.No | Title | Authors/Institution | Features | Key findings | Limitations
3. | Development, Implementation and Usage of an Automated Body Mass Index System | Olajide Patrick O., Musiliyu Kazeem A., Alao Olumuyiwa A.,Owolabi I.E Afe Babalola University | Measurement of BMI Using 4-load cell Wheastone Bridge and PING/HC-SR04 Buzzer with driver circuit for feedback | Provides non-invasive, low-cost BMI measurement Results show strong correlation with manual measurement | Only BMI is measured Tested on 60 students
4. | Patient Assessment and Vital Signs Measurement and Documentation | American Association of Sleep Technologists (AAST) | Standardized methods for measuring/documenting vital signs; includes BMI, SpO₂, OSA risk tools, and questionnaires. | Accurate, consistent assessment improves sleep disorder diagnosis and safety; many external factors influence readings. | Tool accuracy may vary, some methods not suitable for all ages, requires adaptation to facility protocols.

## Slide 9: Literature Review
Sl.No | Title | Authors/Institution | Features | Key findings | Limitations
5. | Study of Health Monitoring System | Megha Chavan, Prof. Prajakta Pardeshi, Dr. S.A. Khoje, Prof. Manasvi Patil – MIT College of Engineering (MITCOE), Pune | Reviews mobile, remote, and wearable health monitoring using IoT, RFID, Bluetooth, ZigBee, GPS for tracking vital signs. | Improves hospital/home monitoring, offers high accuracy and real-time data, reduces cost and workload. | Power use, data security, comfort issues, higher cost with advanced modules, false alarms.

## Slide 10: Methodology
Start
Topic Finalization
Literature Review
Breadboard Testing
Control Algorithm Development
Testing and Validation
Result and Analysis
End
Working?
Yes
No
System Design
Component Selection
Documentation
Component Procurement
Fabrication and Integration

## Slide 11: System Overview
ESP32
Raspberry
pi 4
Ultrasonic Sensor
Pulse rate +
Respiratory rate
Load cell
Temperature
sensor
HMI Display
SPO2

## Slide 12: System Model

## Slide 13: System Model
200CM
40CM
90CM
40CM
30CM
85CM
20CM

## Slide 14: System Flow Chart
System Initialization & Calibration “Raspberry Pi, ESP32, Sensors, Display”
Measure Height ‘HC-SR04 Ultrasonic’
Measure Weight ‘Load cell+HX711’
Pulse & Respiration ‘MAX30100’
SpO2 Measurement ‘MAX30102’
Temperature ‘MLX90614’
Start
Processing in Raspberry Pi
Health Status
Display Basic Health information on screen
Provide Recommendation
End
Data Collection in ESP32
Regular Readings
Irregular Readings

## Slide 15: Process Flow Chart
START
Patient
Data from following sensors HC-SR04, Load Cell, MAX30100, MAX30102, MLX90614
ESP32 Real-time Data Acquisition
Raspberry Pi 4B GUI, Data Processing
Touchscreen Display 'Basic Health Info'
QR Code 'Detailed Report'
END

## Slide 16: BMI= Weight(kg)/ [Height(m)]2
(Tadi Chandrasekhar (BMI-for-age)), 2023)
BMI | Category
＜18.5 | Underweight
18.5-24.9 | Normal weight
25-29.9 | Overweight
≥30 | Obese

## Slide 17
Temperature
Average body temperature: 37 degree Celsius
Temperature | Category
(36.55 C - 37.27 C) | Normal Temperature
Higher than (38 C) | Fever
Below (35 C) | Hypothermia
(Kristin Mitchell), 2024.)

## Slide 18
Pulse Rate
(Elizabeth Christman,2016)
Age Group | Normal Range (bpm) | Below Normal (Bradycardia) | Above Normal (Tachycardia)
School Age (6–12 years) | 70 – 100 | < 70 | > 100
Adolescents (13–18 years) | 60 – 100 | < 60 | > 100
Adults (19–33 years) | 60 – 100 | < 60 | > 100

## Slide 19
Respiration Rate
(Cleveland Clinic, 2025)
Age Group | Normal Range (breaths/min) | Below Normal | Above Normal
19–33 yrs | 12–18 | Slow breathing (Bradypnea) | Fast breathing (Tachypnea)

## Slide 20
Respiration Rate
(Cleveland Clinic, 2025)
Age Group | Normal Range (breaths/min) | Below Normal | Above Normal
19–33 yrs | 12–18 | Slow breathing (Bradypnea) | Fast breathing (Tachypnea)

## Slide 21
SPO2
(John P. Cunha,2019)
Condition | SpO
Normal | 95% to 100% on both adults and children
Abnormal | 80% to 85%
Critical | Below 67%

## Slide 22: Bills of Material
Sl.No | Component | Specification | Component Image | Quantity | Rate (Nu.) | Total rate(Nu.) | Link
1 | Raspberry Pi 4B | Model Name:Raspberry Pi 4 RAM Memory Installed Size : 4 GB CPU Model : ARMv7 Product Dimensions‎ : 3 x 8 x 8 cm; 10 g |  | 1 | 5,759 | 5,759 | https://surl.li/hbretu
2 | Capacitive Touchscreen LCD Display | Product Dimensions : 18 x 10 x 9 cm; 406 g Item model number: ‎7inch (B) Processor Count: ‎1 Memory Clock Speed: 800 MHz |  | 1 | 5,679 | 5,679 | https://surl.lu/qubudb

## Slide 23
Sl.No | Component | Specification | Component Image | Quantity | Rate (Nu.) | Total rate(Nu.) | Link
3 | MAX30100 Heart Rate | Item Weight :‎2 g Product Dimensions: 8 x 4 x 10 cm; 2 g Item model number : BE-001758 |  | 1 | 253 | 253 | https://surl.li/wnprto
4 | Oximeter Sensor Module | Model number : SEN0159 No. of Memory Sticks: 1 Item model number :I‎SEN0159 |  | 1 | 335 | 335 | https://surli.cc/tcwcih
5 | Contactless Temperature sensor | Product Dimensions ‎: 2.9 x 11.7 x 30.1 cm; 400 g Item model no. ‎RC-A-41273 |  | 1 | 1,549 | 1,549 | https://surl.li/owcjpp

## Slide 24
Sl.No | Component | Specification | Component Image | Quantity | Rate (Nu.) | Total rate(Nu.) | Link
6 | 4PCS 50KG Load Cell | Colour:‎4 sensor 1 module No. of Memory Sticks :1 Item Weight : ‎0.06 g Item model no. : FZ6096 |  | 1 | 2,220 | 2,220 | https://surl.li/dvbena
7 | Ultrasonic Distance Sensor | Item Weight: ‎12 g Product Dimensions: 4 x 2 x 1 cm; 12 g Item model no.HC-SR04 |  | 1 | 245 | 245 | https://surl.li/wvbkel
8 | ESP32 WROOM-32 | RAM Memory Installed Size :520 KB Memory Storage Capacity :4 MB CPU Model : Dual-Core |  | 1 | 589 | 589 | https://surl.li/eblppn

## Slide 25
Sl.No | Component | Specification | Component Image | Quantity | Rate (Nu.) | Total rate(Nu.) | Link
9 | Mini UPS Power Bank | Voltage:‎12 Volts Power Source : Corded Electric Batteries Included Lithium Battery : Energy Content 14.8 Watt Hours |  | 1 | 899 | 899 | https://url-shortener.me/55GE
10 | Jumper Wires | Product Dimensions: 4.8 x 12 x 14.6 cm; 80 g |  | 1 | 189 | 189 | https://surl.li/envhfy
11 | Long electronic wire. | Material : ‎Silicone |  | 1 | 325 | 325 | https://surl.li/etvykg

## Slide 26
Sl.No | Component | Specification | Component Image | Quantity | Rate (Nu.) | Total rate(Nu.) | Link
12 | Mini UPS Power Bank | Pure 5V 3A Output with right angle DC connector. 1.5 Mtr. Long dc Dc output cord. |  | 1 | 578 | 578 | https://l1nq.com/sPi9F

## Slide 27: Total budget Calculation
Total cost of component :Nu. 17,970.
Fabrication Cost : Nu. 1,500.
Total Project Cost : Nu .19,470.

## Slide 28: Power Consumption Table
Component | Qty | Operating Voltage | Current Draw (Approx.) | Power = V x I(W) | Notes
Raspberry Pi 4B (4GB) | 1 | 5V | 600 mA (idle) → 1.2 A (full load with display) | ~6.0 W | Main computer, GUI, QR code, logging
Waveshare 7" HDMI Display (Capacitive Touch) | 1 | 5V | ~500 mA | ~2.5 W | Touchscreen & display
ESP32 DevKit | 1 | 3.3V / 5V | ~160 mA (WiFi active peak) | ~0.8 W | Sensor hub & communication
MAX30100 (Pulse + Respiration) | 1 | 1.8V–5V | ~600 µA (active mode) | ~0.003 W | Very low power

## Slide 29: Power Consumption Table
Component | Qty | Operating Voltage | Current Draw (Approx.) | Power = V x I(W) | Notes
MAX30102 (SpO₂) | 1 | 1.8V–5V | ~1 mA (active mode) | ~0.005 W | Very low power
MLX90614 (Temp) | 1 | 3.3V–5V | ~1.5 mA | ~0.008 W | I²C, negligible load
Load Cell (50 kg ×4) + HX711 | 1 set | 5V | ~1.5 mA | ~0.008 W | Active only during reading
HC-SR04 Ultrasonic | 1 | 5V | ~15 mA | ~0.075 W | Short pulses during measurement
Battery Backup Pack (5V, 20,000 mAh typical) | 1 | 5V | Output up to 2.1–3A | Provides ~37 Wh | Powers Pi, display, ESP32, sensors

## Slide 30: Total Power Requirement
1.Base load (Raspberry Pi + Display + ESP32) ≈ 9.3 W.
2.Sensors combined ≈ 0.1 W
3.Total average consumption ≈ 9.5W
Considering
Total Power = 10 W
Runtime Estimate

## Slide 31: Expected Outcomes
Measures BMI, pulse rate, SpO2, respiratory rate, and temperature.
Provides accessible, real-time readings with user-friendly interface.
Generates a simple health index.

## Slide 32: Work Plan (7th Semester)
Activity | Aug |  |  |  | Sep |  |  |  | Oct |  |  |  | Nov |  |  |  | Dec |  |  | 
 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
Topic Finalization |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Literature Review |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Proposal Presentation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
System Design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
First Review |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Components Procurement |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Control Algorithm Development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 33: Work Plan (8th Semester)
Activity | Jan |  |  |  | Feb |  |  |  | Mar |  |  |  | Apr |  |  |  | May |  |  |  | Jun |  |  | 
 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
Fabrication and Integration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Second Review |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototype Designing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Model Testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Third Review |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Report Writing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Report Draft Submission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final Documentation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final Presentation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final Report Submission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 34: Reference
Dhingra1, S., & Sharma2, M. (2019). Real-Time Vital Signs Monitoring System. International Journal of Engineering Research & Technology (IJERT), 8(2278–018). https://www.ijert.org/research/real-time-vital-signs-monitoring-system-IJERTV8IS060475.pdf
Patient Assessment and Vital Signs Measurement and Documentation. (2022). AAST Technical Guideline, 10. https://aastweb.org/wp-content/uploads/2025/03/13.-Patient-Assessment-and-Vital-Signs-Measurement-and-Documentation.pdf
Patrick O, O., & Kazeem A, M. (2020). Development, Implementation and Usage of an Automated Body Mass Index (ABMI) System. Global Scientific Journals, 8(2320–9186). https://www.globalscientificjournal.com/researchpaper/Development_Implementation_and_Usage_of_an_Automated_Body_Mass_Index_ABMI_System.pdf
Professional, C. C. M. (2025, May 7). Vital signs. Cleveland Clinic. https://my.clevelandclinic.org/health/articles/10881-vital-signs
What is a good oxygen rate by age? Causes, symptoms & chart. (2021, October 26). eMedicineHealth. https://www.emedicinehealth.com/what_is_a_good_oxygen_rate_by_age/article_em.htm

## Slide 35: Thank You